## Slide 1
PACIFIC CANBRIAM ENERGY
Production Update System
A centralized data platform for daily and monthly production.
PACIFIC CANBRIAM ENERGY
Engineering Overview · 2026

## Slide 2
THE PROBLEM WE WERE SOLVING
Everything lived in Excel.
02 / 12
Production Update System · Pacific Canbriam Energy
No central database. Every task was its own workbook.
Manual copy-paste between Snowflake, ValNav, Accumap, and spreadsheets
Allocation factors and sales ratios derived by hand — easy to break
Re-running a month was risky; results varied between engineers
Onboarding meant “learn the spreadsheets,” not “learn the data”
No reliable way to audit how a number was produced
Common failure modes
Two engineers editing copies of the same workbook
Mis-pasted columns silently changing totals
Lost public-sales data when re-doing PA
Different answers for the same month

## Slide 3
WHAT WE BUILT
Two deliverables, designed together.
03 / 12
Production Update System · Pacific Canbriam Energy
A new SQL Server data model — and the application that keeps it current.
SQL Server data model
PCE_WM — Well Master
PCE_CDA — daily allocation
PCE_Production — daily production with sequences
Allocation_Factors — PA & Public Sales factors
PCE_Surveys, PCE_TC — surveys and type curves
PyQt5 desktop application
One window, one operation per task
Loads from Snowflake, ValNav, Accumap, Excel
Writes back to the SQL tables — logged & repeatable
Background workers; cancel & summary on every run

## Slide 4
ARCHITECTURE AT A GLANCE
How data flows.
04 / 12
Production Update System · Pacific Canbriam Energy
Snowflake / Prodview
Daily wellhead, gathered, pressures
ValNav
Monthly S2 / condensate factors
Accumap
Monthly public sales gas
Excel imports
Surveys & type curves
PRODUCTION UPDATE
APPLICATION
PyQt5 · ETL · audit log
SQL Server
PCE_WM
PCE_CDA
PCE_Production
Allocation_Factors
PCE_Surveys
PCE_TC

## Slide 5
WHAT THE APPLICATION DOES
Eight operations, one window.
05 / 12
Production Update System · Pacific Canbriam Energy
Well Master
Maintain PCE_WM; import new wells from Snowflake
Prodview / Snowflake
Daily production retrieve into CDA & Production
PA Allocations
Monthly ValNav factors → Allocation_Factors
Public Sales
Accumap sales gas + sales ratios
Survey Import
Directional / log surveys into PCE_Surveys
Type Curves Import
Excel type curves → PCE_TC → Production
Whitson+ Mass Upload
Placeholder for next phase
Exports / Reports
Placeholder for next phase

## Slide 6
SNOWFLAKE → CDA + PRODUCTION REBUILD
Daily flow: Prodview / Snowflake.
06 / 12
Production Update System · Pacific Canbriam Energy
STEP 1
Pick window
Auto: rolling 18 months, ends today − 2 days
STEP 2
Pull Snowflake
ECF, Gas WH, CGR / water, WGR, pressures, allocation
STEP 3
Refresh CDA
Replace matching PCE_CDA rows for the window
STEP 4
Rebuild Production
Sequences, cumulatives, monthly averages
STEP 5
Sync type curves
PCE_TC materialized into PCE_Production
One click. One log. One summary line with row counts and elapsed time.
Exception wells skipped automatically · type-curve & YE2 rows protected

## Slide 7
VALNAV AND ACCUMAP, THE RIGHT WAY
Monthly flow: PA + Public Sales.
07 / 12
Production Update System · Pacific Canbriam Energy
PA Allocations (ValNav) — Writes monthly factors to Allocation_Factors
Public Sales (Accumap) — Merges sales gas; recomputes sales CGR
Auto-propagation — Allocation changes flow to PCE_CDA and PCE_Production
Sales_Gas preserved — Re-running PA does not erase Public Sales data
Idempotent month — Existing month is deleted and rebuilt consistently
The old foot-gun
Doing PA after Public Sales used to wipe Sales_Gas to zero
Engineers had to restore Accumap data by hand
Now: PA reads existing Sales_Gas first, then writes
Public Sales data survives PA reloads

## Slide 8
SUPPORTING FLOWS — NOW ROUTINE
Well Master, Surveys, Type Curves.
08 / 12
Production Update System · Pacific Canbriam Energy
Well Master
Snowflake-driven new well preview
Safe edits with composite-name handling
Honored everywhere — exception flag respected
Surveys
Bulk and mapped Excel layouts
Append vs overwrite behavior is explicit
Unmatched UWIs reported as a CSV
Type Curves
Excel → PCE_TC
Synced into PCE_Production at ImportDate
Protected on every rebuild

## Slide 9
BEFORE VS AFTER
How this saves engineers time.
09 / 12
Production Update System · Pacific Canbriam Energy
Task
Before — Excel only
After — App + SQL
Daily Snowflake → CDA → Production
Half-day spreadsheet round-trip
One dialog, hands-off, logged summary
Monthly PA (ValNav)
Manual factor calc + manual propagation
One dialog; CDA / Production update automatically
Public Sales (Accumap)
Manual UWI matching; risk of erasing PA
One dialog; unmatched UWIs reported; PA preserved
New well onboarding
Update multiple workbooks
Add in Well Master, run Prodview when ready
Survey / Type Curve imports
Manual mapping and pasting
Bulk + mapped imports with audit reports
Re-running a month
Risky; could overwrite
Safe and idempotent
Engineers stop doing data plumbing — and spend time on interpretation.

## Slide 10
BUILT FOR ENGINEERING TRUST
Reliability and auditability.
10 / 12
Production Update System · Pacific Canbriam Energy
Header, step lines, and summary on every run
Row counts and elapsed time recorded
Cancel supported during long jobs
Date caps prevent writing into incomplete days
Exception-flagged wells skipped automatically
Type-curve and YE2 rows protected during rebuilds
Concurrent engineers share the same SQL tables
No silent overwrites; nothing happens off-screen
If something goes wrong, you can read the log and reproduce the result.

## Slide 11
ROADMAP — SHIPPED VALUE, CLEAR NEXT PHASE
What's next.
11 / 12
Production Update System · Pacific Canbriam Energy
Whitson+ Mass Upload — Replace the current placeholder workflow
Exports / Reports — First-class dialog and scheduled extracts
Automated reconciliation — Cross-source checks (Snowflake / Accumap / ValNav)
Smaller asks — Better progress signals, more name-resolution rules
Owners & timelines
Tech lead — to be assigned
Reservoir lead — to be assigned
Pilot users — volunteers welcome

## Slide 12
DISCUSSION
Questions.
12 / 12
Production Update System · Pacific Canbriam Energy
Thanks for your time.
Two minutes of Q&A — or grab me after.
Where to file requests / bugs
<email or ticket link>
Tag: Production Update System
Documentation
docs/USER_GUIDE.md — operators
docs/DEV_GUIDE.md — overview
docs/DEV_GUIDE_LAYOUT.md — deep technical map